## Slide 2: 2018 Integrated Report
Probabilistic Monitoring Chapter Updates
Jason Hill, Emma Jones, Larry Willis, Mary Dail, and Lucy Baker
December 4, 2019

## Slide 3: Basics about ProbMon
Statewide overview program providing collocated biological, chemical, and physical habitat data
Wadeable data used in development of novel tools & analyses
Largely Grant funded program
Study design flexible for future monitoring needs (emerging contaminants)
Headwater stream assessment
  Only DEQ program built to assess and monitor the 65% of Virginia stream miles that are unmonitored by other programs
Notes: Broad purpose- baseline for scale of analyses, statewide overview program
Colocated data is important- development of novel tools/analyses
Largely Grant funded program
Design flexible for future monitoring needs (emerging contaminants)
Headwater stream assessment (only program built to assess and monitor) 65% miles unmonitored by other programs
WADEABLE DATA
Site selection- say random but have pictures as backup
CDF (pictures backup)
Condition estimates
Stressor extent
Relative risk picture backup

## Slide 4: Basics about ProbMon
Notes: Random site selection
CDF (pictures backup)
Condition estimates
Stressor extent
Relative risk picture backup

## Slide 5: Major Changes Since 2016 IR Report
  Executive summary rewrite
  IR window estimates vs statewide status
  Major basin status- micromaps
  Major basin ranks- heatmap
  Relative risk and stressor extent

## Slide 6: Successes
Tish’s slide
Data supports standards are not being violated in things we’ve looked at.
However, we are going to highlight some bad things coming up…

## Slide 8: Percentage of stream miles with water quality parameters exceeding criteria. Figure represents data collected from 2011 - 2016.
Notes: IN line with NRSA results

## Slide 9: Relative risk (2001 – 2016)
Notes: Cancer vs cardiovascular comparison to hammer scale of risk associated with our RR calculations

## Slide 10: IR Window Estimates vs Statewide Status
2011 – 2016 (n = 261)
2001 – 2016 (n = 735)
Notes: Some statistics have always required entire dataset available in order to make meaningful estimates (RR & stressor extent)

## Slide 11: Statewide Status
Stream Size
Major Basin
US EPA Level III
Ecoregion
Statewide
Notes: Equal effort across spatial scales and requires more time to make comparisons among SOME basins
Yearly sample effort based on data requirements to make statistical estimate statewide

## Slide 12: IR Window vs Statewide Status
Biological stream condition index based on VSCI/VCPMI Scores (2011 - 2016, n = 261)
Biological stream condition index based on VSCI/VCPMI Scores (2001 - 2016, n = 735)

## Slide 13: Biological condition by stream size category (2001 – 2016)
Notes: Hammer conf limits, unoverlapping indicates significance

## Slide 14: Biological condition by US Level III Ecoregions (2001 – 2016)
Mid-Atlantic Coastal Plain Ecoregion was not included due to insufficient data.

## Slide 15: Biological condition by major river basins (2001 – 2016)

## Slide 16: Parameters without WQS: major basin status using micromaps
VSCI/VCPMI status by basin. The vertical dashed line at 60 highlights the biologic assessment threshold
VSCI/VCPMI status by basin

## Slide 17: Basin Rank
1 = MOST suboptimal stream miles
11 = LEAST suboptimal stream miles

## Slide 18: Other uses of ProbMon
Environmental Disaster Interpretation (Dan River Coal Ash)
Biomonitoring Improvement (Validation of VCPMI & VSCI)
TMDL support (Benthic Stressor Analysis Tool)
Permit Tool
Tolerance Assignment (BCG, Genus level biological tool development)
Change analysis

## Slide 19
Questions?

## Slide 20: Parameters without WQS: major basin status using micromaps
Vertical dashed lines represent the percent of stream miles across Virginia with suboptimal habitat disturbance and biologic condition below the assessment threshold, respectively.
Percent of stream miles with suboptimal habitat disturbance

## Slide 21: Parameters without WQS: major basin status using micromaps
Vertical dashed lines represent the percent of stream miles across Virginia with suboptimal total phosphorus and biologic condition below the assessment threshold, respectively.
Percent of stream miles with suboptimal total phosphorus

## Slide 22: Parameters without WQS: major basin status using micromaps
Vertical dashed lines represent the percent of stream miles across Virginia with suboptimal ionic strength and biologic condition below the assessment threshold, respectively.
Percent of stream miles with suboptimal ionic strength

## Slide 23: Temporal Variability
VSCI/VCPMI status in James River and Big Sandy River basins with increasing n.

## Slide 24: Stressor extent (2011 – 2016)

## Slide 25: Stressor extent, all condition classes (2011 – 2016)

## Slide 26
Virginia’s Freshwater Resources
Target population perennial freshwater river and streams
NHD circa 1999 sample frame is 49,142 miles

## Slide 27
EMAP
640 km
2
Hexagon
90
km
2
13
km
2
1.8
km
2
13 km
2
Hexagon
EMAP Hexagon
640 km
2
Hexagon
90
km
2
13
km
2
1.8
km
2
640 km
2
Hexagon
90
km
2
13
km
2
1.8
km
2
90 km2
13
km2
13 km
2
Hexagon
13 km
2
Hexagon
13 km
2
Hexagon
Site Selection

## Slide 28
Water Quality Stressors
Relative Risk and Attributable Risk Calculations
Borrowed terminology from the medical field
Report RR greater than 1 (CI included)

## Slide 29
Statewide Relative Risk
Pr(Poor VSCI/CPMI, given poor sediment condition) RR = --------------------------------------------------------------- Pr(Poor VSCI/CPMI, given good sediment condition)

## Slide 30
Innovative Monitoring
Sediment endpoint in many biological studies
Relative bed stability=quantitative habitat data

## Slide 31: Stressor Screening Results

## Slide 32: CDF Curves
50th percentile is 0.02 mg/L
95th percentile is 0.1 mg/L
0.02 mg/L

## Slide 33: Stressor Distribution
Notes: 80% below 1